## Slide 1: Small Engine tool, parts & Equipment
Dana mills

## Slide 2: ENGINE PRECISION MEASURING TOOLS

## Slide 3: Engine precision measuring tools
Are used to accurately measure components when very small tolerances are allowed
  to make sure components conform to standards and all parts fit together once the product is built
Fun fact: tolerance refers to the dimensions and or properties having some variation without affecting the functions of the engine

## Slide 5: Engine precision measuring tools
Include:
  micrometers
  telescoping gauge
  small hole gauges
  digital caliper
  feeler gauges
  dial indicator
  surface plate
  torque wrench

## Slide 6: Micrometers
Are handheld devices used to measure the thickness of valve stems and other materials
  down to one thousandth of an inch or to one ten thousandths of an inch
Consist of a C-shaped head and a rotating dial handle with measurements
Can be calibrated by a technician
Require following the manufacturer’s directions when using or calibrating

## Slide 7: micrometers
Precisely measure components in which tolerances are critical, including the following:
  pistons
  crankshafts
  valve stems
  cylinders
  rings
  other small engine components

## Slide 8: micrometers
Types of micrometers include:
  outside micrometer
    measures the outside diameter of round objects and the thickness of flat pieces
  inside micrometer
    measures the inside diameter of a cylinder or ring
  depth micrometer
    measures the depths of holes, grooves and slots
  Vernier micrometer
    measures more precisely than standard micrometers

## Slide 9: Outside Micrometer

## Slide 10: Parts of micrometer

## Slide 11: Micrometer units
May be metric or imperial
  imperial units are known as customary units (i.e., inches, feet, miles, etc.)
Are as follows:
  standard micrometers are graduated in thousandths of an inch (.001”)
  Vernier micrometers are graduate in ten-thousands of an inch (.0001”)
  metric micrometers are graduated in hundredths of a millimeter (.01mm)

## Slide 12: Reading a micrometer
Involves understanding the following components:
  sleeve
    does not move
  thimble
    rotates around the sleeve

## Slide 13: Reading a micrometer (1” standard)
Sleeve
  is divided into 40 equal parts
  each line represents 0.025”
  every fourth line is numbered and represents 0.1”
Thimble
  is divided into 25 equal parts
  each line represents 0.001”
  every fifth line is marked and represents 0.005”

## Slide 14: Examples

## Slide 15: Micrometer maintenance
Includes:
  regularly wiping the spindle and both measuring faces with a dry cloth in order to keep clean
  applying multipurpose oil to prevent rusting
  avoiding storing in humid climates or extreme temperatures
  avoiding leaving the spindle and anvil in contact
    could alter the accuracy
  store in a protective case when not in use
May be necessary if the micrometer is dropped
  which can alter the accuracy of the measurement

## Slide 16: Micrometer Use & safety
Include:
  cleaning the anvil before measuring
  holding the micrometer square and level
    if it is at an angle, measurement will not be accurate
  holding the micrometer with the dominant hand
  making certain to not overtighten the thimble
  using the micrometer according to manufacturer’s instructions

## Slide 17: Telescoping gauges
Are transfer measuring tools, which transfer a measurement to a micrometer
Are made to measure holes where inside micrometers are unable to fit
Expand under spring tension within a hole to be measured and then locked into position after the measurement has been taken
Does not provide a direct measurement

## Slide 18: Telescoping gauge

## Slide 19: Maintenance
Telescoping Gauge Maintenance Includes:
  cleaning after each use
  avoiding storing in the same area as hand tools
    which may bump or damage the gauges
  storing in a protective case when not in use
  avoiding exposure to high temperatures
  repairing at an authorized facility

## Slide 20: Use & Safety
ensuring the handle is in line with the center-line of the cylinder being measured
  ends must be exactly aligned with the true diameter of the cylinder
moving the gauge up and down the cylinder causing the spring tension to reach a true diameter
  when a true diameter has been reached, gently tighten the lock screw, then once it is locked, tilt the handle so the tool can be removed from the cylinder and a measurement can be taken with a micrometer
using the telescoping gauge according to manufacturer’s instructions

## Slide 21: Small hole gauges
Are similar to a telescoping gauge
Are measuring tools with an expandable head
Are used for measuring small diameter holes which a telescoping gauge cannot fit into
Require a working micrometer to read the measurements taken

## Slide 22: Small hole gauge

## Slide 23: Maintenance
  cleaning after each use
  avoiding storing in the same area as hand tools
    which can bump and damage the gauges
  storing in a protective case when not in use
  avoiding exposure to high temperatures
  only repairing at an authorized facility

## Slide 24: Proper Use & safety
  placing the head of the gauge into the hole which needs to be measured and turning the handle until the sides of the head are touching the sides of the hole, then measuring with an outside micrometer
  using the gauge according to manufacturer’s instructions

## Slide 25: Feeler gauges
AKA “thickness gauges”
Rely on the users sense of touch for measurements and are used to measure small spaces between surfaces, including:
  spark plug
  crankshaft endplay
  piston ring
Consists of metal leaves which vary in thickness and each leaf has its own measurement on the handle

## Slide 26: Feeler gauges

## Slide 27: Units
Typically in the thousandths of an inch and/or hundredths of a milliliter
Typically laser-etched on the end of the blade

## Slide 28: Maintenance
Wiping clean before and after each use
Avoid taking measurements over any markings on blades
  This avoids unnecessary wear of markings

## Slide 29: Proper use & Safety
  keeping blades folded together and stored in their protective housing when not in use
  avoiding various components which may cause injuries from pinching
  keeping fingers a safe distance from the parts being measured
  using caution when working around electrical components

## Slide 30: Digital caliper
Is a precision measuring tool which is used to measure internal and external distances
Digitally displays measurements on an LCD screen
Can be measured in millimeters or inches (metric/imperial)

## Slide 31: Types of calipers
  Vernier calipers
    have a sliding scale along the top and bottom
  dial calipers
    display measurement with a pointer
  electronic digital calipers
    have an LCD screen which displays measurements
What kind do we have?

## Slide 32: Digital caliper

## Slide 33: Parts of caliper

## Slide 34: Maintenance
  cleaning after each use
  avoiding storing in the same area as hand tools
    which can bump and damage the caliper
  storing in a protective case when not in use
  avoiding exposure to high temperatures
  only repairing at an authorized facility

## Slide 35: Use & safety
  using the caliper on work pieces which have been de-energized and are no longer moving
  using the caliper according to manufacturer’s directions
  zeroing the dial each time after the caliper is used

## Slide 36: Dial indicators
Used to measure movements of components in fractions of an inch or millimeters
Consist of a dial attached to a needle
Can be used to determine crankshaft end play

## Slide 37: Types of dial indicators
  probe indicator
    dial and needle connected to gears inside the indicator
    measures in millimeters or inches
  dial test indicator
    measures smaller range than the probe indicator
  digital indicator
    uses a digital readout instead of a clock face
      making recording data much easier
    measures in millimeters or inches

## Slide 38: Dial indicator

## Slide 39: Adjustments
setting the dial indicator to zero by rotating the bevel until the zero line is directly under the needle

## Slide 40: Maintenance
  cleaning after each use
  avoiding storing in the same area with hand tools
    which can bump and damage the gauges
  storing in a protective case when not in use
  avoiding exposure to high temperatures
  repairing and calibrating at an authorized facility
    technicians should never attempt to repair broken dial indicators on their own

## Slide 41: Use & safety
  always keeping hands clear of rotating machinery during use
  stopping all moving parts to be measured before attaching the dial indicator
  attaching a dial indicator according to manufacturer’s instructions

## Slide 42: Torque wrench
Measures the specific torque applied to a fastener such as a bolt
  torque is the force which causes rotation
Helps ensure a fastener will not break

## Slide 43: Types of torque wrenches
Include:
  electric
  click
  beam
  plumber
  hydraulic
  deflecting beam

## Slide 45: Maintenance
  checking periodically for wear or defective parts
    the more the wrench is used the more wear it will have
  keeping the wrench in a case to protect the tool from dust, grime and other hazards
  keeping the wrench dry and clean
  storing wrenches with a spring mechanism at the minimum setting when not in use
    leaving wrenches on a high setting can distort the calibration causing inaccurate measurements

## Slide 46: Use & safety
  reading all instructions
    each torque wrench has different instructions for use, maintenance and service

## Slide 47: Surface plate
Is a solid, flat plate which is used for inspections, layout and setting up tools
Helps measure whether an object is flat, level or neither
  for example, bends which are not obvious to the eye

## Slide 48: Surface plate

## Slide 49: Maintenance
  cleaning after each use
  repairing and calibrating according to the manufacturer’s manual

## Slide 50: Use & safety
  oiling the plate if it has not been used for an extended period of time
    wiping the surface with a small amount of oil so it does not rust
  never hammering or completing any other operations on the plate
    could cause damage to the plate